## Slide 1: Workload-Aware Capacitorless LDO with Adaptive Biasing
ANALOG / MIXED-SIGNAL IC DESIGN · PROJECT STATUS
A flipped-voltage-follower (FVF) based output-capacitorless regulator for bursty Edge-AI / AIoT power domains, designed in the open SkyWater sky130 PDK for a Tiny Tapeout shuttle.
Mentor: Dr. Jyotishman Saikia · Co-Mentor: Dr. Vaegae Naveen Kumar
Dept. of Micro and Nanoelectronics, SENSE
Phase 2 status · Oct 2026

## Slide 2: Where a fast, capacitorless LDO earns its place
TARGETED APPLICATIONS
Edge-AI sensor nodes
Stable local rails across sleep → sensing → inference → communication transitions.
Edge-AI cameras & agri/industrial sensing
Absorbs sudden current spikes from on-device image or signal processing bursts.
Mixed-signal SoCs
Shields sensitive analog and sensor front-ends from digital switching noise on a shared supply.
AIoT / dynamic voltage scaling
Fast, low-IQ wake-up stability for devices that scale voltage with workload.
Proposal §2.2 · Final application

## Slide 3: Workload-Aware Digitally Assisted Fast-Transient Capacitorless LDO with Adaptive Biasing for Edge-AI Systems
PROPOSED TOPIC
Hypothesis: adaptive biasing combined with a fast transient-boost path lets an output-capacitorless LDO respond faster to sudden load changes and stay energy-efficient, without a large external output capacitor — built and verified in SkyWater sky130 (open PDK), with a Tiny Tapeout shuttle as the tapeout route.
0–10mA
Target load range
No C_OUT
Output-capacitorless topology
4-bit
Digital voltage scaling (DVS)

## Slide 4: Four blocks, built up in order
OVERALL PROJECT PLAN
BUILT & VALIDATED
FVF + Pass Element
Flipped voltage follower driving the PMOS pass device — the base regulation loop.
BUILT · REV C
Transient-Boost Path
Detects sudden VOUT excursions and kicks extra drive onto the pass device.
BUILT · REV D
Adaptive Bias & Stability
Scales IBIAS with load to trade quiescent current for speed only when needed.
BUILT · RTL + AMS
4-bit DVS / Control
Digital output-voltage selection, plus a workload-hint input to pre-bias the loop.
Devices characterized (gm/Id tables) and specs set
Baseline FVF-only LDO kept as reference (boost off via ben pin)
Transient boost, adaptive bias and DVS all built and simulated
45-point PVT sweep running; hot-corner leakage is the open issue
Next: layout, PEX and AMS sign-off
Characterize on silicon via a Tiny Tapeout shuttle

## Slide 5: PDK, flow and the four blocks
CURRENT PROGRESS
PDK & flow
SCL, TSMC22 and GF55 models unavailable; ICsprout55 ships no SPICE models
Chosen: SkyWater sky130 (open, silicon-proven), tapeout via Tiny Tapeout
xschem + ngspice: 18-cell library, levels L0–L4, one schematic + symbol per block
AMS: dvs_ctrl RTL runs inside ngspice (Verilator + d_cosim); PVT sweeps scripted
What's built
FVF loop + replica VSET generator: PM ≥ 85° (TT), 1.07 mV/mA load regulation
Transient boost: AC-coupled dip detector + ×20 gate pull-down, about halves undershoot
Adaptive bias: 1/500 pass replica makes loop bias track load; Iq 270 → 163 µA
4-bit DVS: R-DAC 1.00–1.45 V in 30 mV steps + slew-limited controller with workload hint

## Slide 6: Boost and adaptive bias: Rev D results
CURRENT PROGRESS · KEY FINDING
Metric | Without assist | Rev D (boost + adaptive bias)
Undershoot, 0.1 → 10 mA in 100 ns | 267 mV | 118 mV
Edge-AI burst, 1.3 → 9.6 mA in 10 ns | 534 mV | 334 mV
Quiescent current | 270 µA (fixed bias) | 163 µA
On the same netlist, the transient boost (switched by the ben pin) more than halves the 100 ns undershoot and cuts the Edge-AI burst dip by 37 %, while adaptive bias lowers standby current by 40 %. Trade-offs: light-load PSRR at 1 MHz drops about 10 dB, and phase margin falls to 25° at the hottest light-load corner, which is the next fix. The real dvs_ctrl RTL, co-simulated in ngspice, pre-raises VOUT on the workload hint before the burst.
sky130 TT · 27 °C · VIN 1.8 V · ngspice

## Slide 7: What we fix next
OPEN ISSUES & NEXT STEPS
01
Hot-corner leakage (125 °C, light load): add a shunt clamp or gain-stage driver
02
+12–15 mV DC offset across DVS codes: improve replica matching and OTA gain
03
PSRR (−30 dB at 1 kHz) and line regulation (24 mV/V) are limited by the single-stage FVF loop
04
Swap ideal R/C for sky130 MIM and poly devices; run Monte-Carlo mismatch
05
Layout → DRC / LVS / PEX → Tiny Tapeout analog submission (≤ 2×2 tiles)

## Slide 8: What the project delivers
EXPECTED OUTCOMES
01
A basic and an improved output-capacitorless LDO, both realized in the target process
02
A head-to-head comparison of fixed-bias, adaptive-bias, and fully-assisted designs on performance and power
03
Validation against Edge-AI workload current patterns: sleep, sensing, inference, communication
04
Complete layout with DRC / LVS / PEX / AMS verification, and a GDSII if the schedule allows
05
Silicon characterization on a Tiny Tapeout shuttle, otherwise sign-off by post-layout simulation

## Slide 9: One-year execution plan
PROJECT TIMELINE
Phase | Period | Activities
1 | Aug–Sep 2026 | Literature review, PDK / device characterization, specifications
2 — now | Oct–Dec 2026 | Baseline FVF + adaptive bias + transient assist + DVS
3 | Jan–Mar 2027 | AMS / PVT / stability / PSRR / workload optimization
4 | Apr–May 2027 | Custom layout, integration, PEX
5 | Jun–Jul 2027 | DRC / LVS / ERC, AMS sign-off, GDSII / tape-out
6 | Aug 2027 onward | Fabrication return, PCB bring-up, silicon characterization, report
Fabrication and silicon testing proceed only if the MPW shuttle schedule allows it.
One-year execution plan · proposal §3